## Slide 1: AWS IoT Workshop with LinkIt One
John Chang
Ecosystem Solution Architect
johnchan@amazon.com

## Slide 2: What Is AWS IoT
AWS IoT is considered a beta service as defined in the Service Terms

## Slide 3: MediaTek LinkIt™ ONE and Grove IoT Starter Kit Powered by AWS
Product Page
  https://labs.mediatek.com/site/global/developer_tools/mediatek_linkit/hdk_intro/aws_kit/index.gsp
LinkIt ONE Connect to AWS IoT Services
  https://github.com/MediaTek-Labs/aws_mbedtls_mqtt

## Slide 4: Get Started with AWS IoT Services on the LinkIt™ ONE Development Platform
Setup for development on LinkIt ONE using the Arduino IDE as described here.
Install and configure the AWS IoT services command line interface (CLI) and a MQTT client.
Add the mbed TSL library for LinkIt ONE to your Arduino IDE.
Provision your AWS certificates to the LinkIt ONE development board.
Create your LinkIt ONE application and run it on your board.

## Slide 5: Setup for development on LinkIt ONE using the Arduino IDE

## Slide 6: Get Started with the LinkIt™ ONE Development Platform
Install Arduino 1.5.7
  https://www.arduino.cc/en/Main/OldSoftwareReleases#1.5.x
Windows PC
  Download the Arduino IDE
  Download the LinkIt ONE SDK
Mac
  Download the Arduino IDE
  Download the LinkIt ONE SDK (LinkIt ONE SDK can be used on Mac OSX 10.09 and 10.10)

## Slide 7: Install the Arduino IDE and LinkIt ONE SDK
Windows PC
  https://labs.mediatek.com/site/global/developer_tools/mediatek_linkit/get-started/windows/install/
MAC
  https://labs.mediatek.com/site/global/developer_tools/mediatek_linkit/get-started/mac/install/

## Slide 8: Update Your Board’s Firmware
Set the board to Mass Storage Bootup mode
Run the LinkIt ONE Firmware Updater Application
  https://labs.mediatek.com/site/global/developer_tools/mediatek_linkit/get-started/windows/update/

## Slide 9: Configure the Arduino IDE
Windows PC
  https://labs.mediatek.com/site/global/developer_tools/mediatek_linkit/get-started/windows/configure/
MAC
  https://labs.mediatek.com/site/global/developer_tools/mediatek_linkit/get-started/mac/configure/
Create and Run Your First Sketch
  n Arduino IDE on the File menu point to Examples, then 01. Basics and click Blink, this opens the Blink example.

## Slide 10: Install and configure the AWS IoT services command line interface (CLI) and a MQTT client

## Slide 11: Create a Device in the Thing Registry
Install the AWS CLI
  Getting Set Up with the AWS Command Line Interface.
Create a thing named ”XXXXX"
  aws iot create-thing --thing-name “XXXXX”
Confirm the thing has been created
  aws iot list-things

## Slide 12: Secure Communication Between a Device and AWS IoT
Provision a Certificate
  aws iot create-keys-and-certificate --set-as-active --output text
  output of the command contains the certificate, the certificate's ARN, the public key, and the private key.
Save the certificate to a file
  aws iot describe-certificate --certificate-id "certificate-id" --output text --query certificateDescription.certificatePem > cert.pem
  The certificate-id is part of the certificate ARN

## Slide 13: Secure Communication Between a Device and AWS IoT
Create and Attach an AWS IoT Policy to Your Certificate
  Policy Document
    {
    "Version": "2012-10-17",
    "Statement": [{
    "Effect": "Allow",
    "Action":["iot:*"],
    "Resource": ["*"]
    }]
    }
Create the AWS IoT policy
  aws iot create-policy --policy-name "AllowAllIotOperationsPolicy" --policy-document file://AllowAllIotOperations.json

## Slide 14: Secure Communication Between a Device and AWS IoT
Attach the policy to your certificate
  aws iot attach-principal-policy --principal "certificate-arn" --policy-name "AllowAllIotOperationsPolicy"
Attach your Certificate to Your Device
  aws iot attach-thing-principal --thing-name ”XXXXX" --principal "certificate-arn"

## Slide 15: Setting Up CloudWatch Logs
Create an IAM Role for Logging
  Role policy
    {
    "Version": "2012-10-17",
    "Statement": [
    {
    "Effect": "Allow",
    "Action": [
    "logs:CreateLogGroup",
    "logs:CreateLogStream",
    "logs:PutLogEvents",
    "logs:PutMetricFilter",
    "logs:PutRetentionPolicy"
    ],
    "Resource": [
    "*"
    ]
    }
    ]
    }

## Slide 16: Setting Up CloudWatch Logs
Create an IAM Role for Logging
  Trust policy
    {
    "Version": "2012-10-17",
    "Statement": [
    {
    "Sid": "",
    "Effect": "Allow",
    "Principal": {
    "Service": "iot.amazonaws.com"
    },
    "Action": "sts:AssumeRole"
    }
    ]
    }

## Slide 17: Setting Up CloudWatch Logs
Register the Logging Role with AWS IoT
  aws iot set-logging-options --logging-options-payload roleArn=”arn:aws:iam::<your-aws-account-num>:role/IoTLoggingRole”,logLevel=”INFO”
Log level
  DEBUG provides the most detailed information of AWS IoT activity.
  INFO provides a summarized view of most actions. This is sufficient for most users.
  ERROR provides error cases only.
  DISABLED removes logging altogether, but keeps your logging role intact.

## Slide 18: Add the mbed TSL library for LinkIt ONE to your Arduino IDE

## Slide 19: Create and run your first AWS IoT sketch

## Slide 20: Provision your AWS certificates to the LinkIt ONE development board
Copy the .pem files into the LinkIt ONE development board’s flash storage
  switch it into Mass Storage mode, as shown below
  Navigate to Computer, then Devices and Removable Storage. Open the removable disk drive corresponding to the LinkIt ONE development board.

## Slide 21: Provision your AWS certificates to the LinkIt ONE development board
Copy the .pem files into the LinkIt ONE development board’s flash storage
  Copy the certificates you saved in .pem format into the removable disk drive.
  return the board to Normal Bootup switch mode (UART) and proceed with the sketch development.

## Slide 22: Add the mbed TLS and AWS IoT Services MQTT libraries to the Arduino IDE
AWS LinkIt ONE sketch development requires the mbed TLS and AWS IoT Services MQTT libraries to support MQTT communication
  mbed TLS enables SSL/TLS capabilities for (embedded) products
  find the source Arduino project (aws_paho_mqtt.ino) and the supporting libraries in the aws_mbedtls_mqtt repository on GitHub.
  Copy the libraries into your Arduino/libraries folder.

## Slide 23: Programming your application
Open aws_paho_mqtt.ino sketch (from the aws_mbedtls_mqtt repository on GitHub )
Resolve hostname for the IP address. Run the following command to identify the IP address,
  ping g.us-east-1.pb.iot.amazonaws.com
  and Change the variable VMSTR IP_ADDRESS to the IP address you’ve just identified
Provide the certificate names by matching the following variables
  char cafileName[] = "A5.pem"; //root CA
  char clientCRTName[] = "cert.pem";
  char clientKeyName[] = "privatekey.pem";

## Slide 24: Programming your application (cont.)
Replace the topic name for the following variables
  subParams.pTopic = "yourTopicName";
  Params.pTopic = "yourTopicName";
Upload the sketch to the LinkIt ONE development board.
  Tools  Board  LinkIt One
  Tools  Port
Launch the Serial Monitor on the Arduino IDE
  Tools  Port
  Tools  Serial Monitor

## Slide 25: Configure and Test Rules

## Slide 26: Create an IAM Role for AWS IoT
Assume Role policy
  {
  "Version": "2012-10-17",
  "Statement": [{
  "Sid": "",
  "Effect": "Allow",
  "Principal": {
  "Service": "iot.amazonaws.com"
  },
  "Action": "sts:AssumeRole"
  }]
  }
aws iam create-role --role-name "iot-actions-role" --assume-role-policy-document file://path-to-file/trust-policy-file

## Slide 27: Grant Permissions to the Role
Create an IAM policy and attach the policy to your role
  {
  "Version": "2012-10-17",
  "Statement": [{
  "Effect": "Allow",
  "Action": [ "dynamodb:*", "lambda:InvokeFunction"],
  "Resource": ["*"]
  }]
  }
aws iam create-policy --policy-name "iot-actions-policy" --policy-document file://IAM-policy-document-file-path
aws iam attach-role-policy --role-name "iot-actions-role" --policy-arn "policy-ARN"

## Slide 28: Create a Rule to Insert a Message into a DynamoDB Table
Create a DynamoDB table has a hash attribute of type String and a range attribute of type String.
Create an IoT Rule
  {
  "sql": "SELECT * FROM 'topic/test'",
  "ruleDisabled": false,
  "actions": [{
  "dynamoDB": {
  "tableName": "sampleTable",
  "hashKeyField": "key",
  "hashKeyValue": "${topic(2)}",
  "rangeKeyField": "timestamp",
  "rangeKeyValue": "${timestamp()}",
  "roleArn": "arn:aws:iam::123456789012:role/iot-actions-role"
  }
  }]
  }
aws iot create-topic-rule --rule-name "saveToDynamoDB" --topic-rule-payload file://path-to-file/DynamoDbRule

## Slide 29: Connect Grove Temperature Sensor
Grove - Temperature Sensor V1.2
  http://www.seeedstudio.com/wiki/Grove_-_Temperature_Sensor_V1.2

## Slide 30: References
http://docs.aws.amazon.com/iot/latest/developerguide/iot-quickstart.html
https://labs.mediatek.com/site/global/developer_tools/mediatek_linkit/get-started/aws/get-started/index.gsp
http://www.seeedstudio.com/wiki/Grove_-_Temperature_Sensor_V1.2
http://www.slideshare.net/AmazonWebServices/mbl205-new-everything-you-want-to-know-about-aws-iot

## Slide 31: Challenge – Win $100 USD AWS Credit !!
請使用 IoT Starter Kit 當中的 Moisture Sensor，建立一個自動記錄溼度的AWS IoT 解決方案，並將資料記錄在 DynamoDB中
完成之後請錄製一段短片，內容必須包括
  接上Moisture Sensor的LinkIt One開發版以及接收資料的DynamoDB.
  將Moisture Sensor插入水中，從DynamoDB可以收到變化的數值
將短片上傳到Youtube，標題為”我的 IoT 濕度計”，並將影片連結email到 johnchan@amazon.com 驗證。
[Hint]
  https://github.com/Seeed-Studio/Moisture_Sensor